## Slide 1
A2
ns-3 Setup &
3GPP XR Pose Traffic Model
A deterministic uplink baseline based on 3GPP TR 26.926 §5.9.2
[Your Name] · [Student ID]
Week 7 · 10-minute presentation
ns-3.44 | Ubuntu 22.04.5 LTS | x86-64

## Slide 2
ENVIRONMENT
Setup and reproducibility
A2 · ns-3 Setup & Traffic Model
02
ns-3.44
Simulator version
Ubuntu 22.04.5
Linux platform · x86-64
60 s
Traffic duration · 6,000 packets
Build and run
$ ./ns3 build xr-pose-uplink
$ ./ns3 run xr-pose-uplink
$ python3 scratch/plot-xr-pose-results.py --prefix xr-pose-uplink
What broke?
Restricted ccache directory
→ built with CCACHE_DISABLE=1
Matplotlib GUI warnings
→ switched plotting backend to Agg

## Slide 3
TRAFFIC MODEL
3GPP Pose uplink model
A2 · ns-3 Setup & Traffic Model
03
Specified by §5.9.2
Pose is available to the application every 1 ms (1 kHz).
Each IP packet is 100 bytes: 60-byte payload + 40-byte headers.
The latest pose is reported every 10 ms (100 Hz).
Target uplink latency is no greater than 10 ms.
Experimental choices
UDP/IPv4 over a point-to-point baseline link.
One XR device and one application server.
Fixed pose: position (1,1,1.2), quaternion (0,0,0,1).
The timestamp changes every sample; motion is not required.
Source: 3GPP TR 26.926 V18.2.0, §5.9.2 — Pose Uplink Model

## Slide 4
IMPLEMENTATION
Topology and 100-byte packet format
A2 · ns-3 Setup & Traffic Model
04
XR DEVICE
10.1.1.1
UDP/IPv4 →
10 Mbps · 1 ms one-way
SERVER
10.1.1.2
100-byte IPv4 packet
IPv4 header
20 B
UDP
8 B
Report header
12 B
Pose payload
60 B
Pose payload: position 12 B · quaternion 16 B · sample time 8 B · device ID 4 B · reserved 20 B
Sequence 4 B + send time 8 B
Network delay = receive time − send time
Pose age = receive time − sample time
PCAP adds a 2-byte PPP header: captured frame = 102 B

## Slide 5
RESULTS
Traffic-model verification: PMF and CDF
A2 · ns-3 Setup & Traffic Model
05
P(size = 100 B) = 1
P(inter-arrival = 10 ms) = 1

## Slide 6
RESULTS
Evidence from my ns-3 run
A2 · ns-3 Setup & Traffic Model
06
80 kbps
Measured IP offered rate
1.0816 ms
Mean and maximum delay
100%
Packets meeting ≤10 ms

## Slide 7
WIRESHARK
PCAP proof and packet accounting
A2 · ns-3 Setup & Traffic Model
07
1.000000 IP (0x0021), length 102: 10.1.1.1 → 10.1.1.2 UDP, length 72
1.010000 IP (0x0021), length 102: 10.1.1.1 → 10.1.1.2 UDP, length 72
1.020000 IP (0x0021), length 102: 10.1.1.1 → 10.1.1.2 UDP, length 72
What to verify in Wireshark
Filter: udp.port == 5000
Time delta between packets: 0.010 s
IPv4 total length: 100 bytes
UDP length: 80 bytes; UDP payload: 72 bytes
Why does PCAP show 102 B?
2 B
+
100 B
PPP header
IPv4 packet
= 102-byte captured frame

## Slide 8
TAKEAWAYS
Conclusion
A2 · ns-3 Setup & Traffic Model
08
The implemented traffic model matches the configured 3GPP baseline.
6,000 / 6,000
Packets sent / received · 0% loss
100 B · 10 ms
Deterministic size and reporting period
1.0816 ms
Well below the 10 ms latency target
Why UDP?
Pose updates become stale quickly. UDP avoids retransmission, acknowledgements, and head-of-line blocking; the next fresh pose is more useful than a delayed old pose.
Next step
Add movement, wireless loss, jitter, or congestion only after the baseline traffic model is verified.
Questions?